This section lists units of operating equipment that are to be overhauled or retired at the period specified. Removal of equipment for overhaul may be accomplished at the inspection nearest the time when overhaul is due unless otherwise specified in TM 1-1500-328-23.

1. Overhaul Interval. The maximum authorized operating time or calendar interval of parts prior to removal for overhaul at category of maintenance authorized in accordance with the Maintenance Allocation Chart.

2. Retirement Schedule. The operating time or calendar interval specified for removal, condemnation, and disposal of parts in accordance with applicable directives.

WARNING

The Retirement Interval of the components/assemblies listed in the table below shall not be exceeded.

NOTE

Due to increased operational tempo, the components in the table below are reaching their overhaul interval sooner than expected. This has resulted in a low stock availability of those components. Present Overhaul Intervals were established to maintain reliability of the items listed. By using the Interim Overhaul Intervals, components will accumulate more wear and damage before the item is overhauled. This may result in a medium to long-term negative effect on readiness. Scheduled and planned overhauls will be shifted to unscheduled maintenance, which makes maintenance management more difficult. It is recommended, when possible, to continue to change out components when the hours accumulated reach the Present Overhaul Interval.

Table 1. OVERHAUL AND RETIREMENT SCHEDULE

|  |  | INTERIM | PRESENT |  |
| --- | --- | --- | --- | --- |
|  |  | OVERHAUL INTERVAL | OVERHAUL INTERVAL | RETIREMENT INTERVAL |
| PART NUMBER AND ITEM | NOMENCLATURE | (HOURS) | (HOURS | (HOURS) |
| AIRFRAME |  |  |  |  |
| 206-032-004-157 206-032-004-171 | Tailboom (0.040) | On Condition | On Condition |  |
| 206-032-004-177 406-961-024-149 | Tailboom (0.063) | On Condition | On Condition |  |
| MAIN ROTOR |  |  |  |  |
| 406-010-100-121 | Main Rotor Hub Assembly | On Condition | 2400 |  |
| 406-010-101-109 | Main Rotor Yoke |  |  | 4800 |
| 406-010-108-115 | Main Rotor Grip |  |  | 4550 |
|  | Continued |  |  |  |
| 406-010-111-105, -113 | Main Rotor Pitch Horn |  |  | 4800 |
| 406-010-115-109 | Main Rotor Upper Plate |  |  | 3600 |
| 406-010-117-109 | Main Rotor Lower Plate |  |  | 3600 |
| 406-015-101-113 | Main Rotor Blade |  |  | On Condition |
| 406-310-101-103 | Shear Bearing Assy |  |  | 2850 |
| 406-010-126-101 | Drive Ring Set |  |  | 3600 |
| MAIN ROTOR CONTROLS |  |  |  |  |
| 206-076-031-105 | Collective Actuator | On Condition | On Condition |  |
| 406-010-401-103, -111 | Swashplate and Support Assy | On Condition | 2400 |  |
| 406-010-411-105, -113 | Swashplate Outer Ring |  |  | 4800 |
| 406-010-410-109, -115 | Swashplate Inner Ring |  |  | 4800 |
| 406-010-417-101, -105 | Swashplate Bearing and Liner |  |  | 4800 |
| 406-010-425-101, -105 | Swashplate Drive Lever |  |  | 4800 |
| 406-010-426-101, -105 | Swashplate Drive Link |  |  | 4800 |
| 406-010-427-105, -107 | Swashplate Gimbal Ring |  |  | 4800 |
| 406-010-428-101, -107 | Swashplate Drive Hub Set |  |  | 4800 |
| 406-010-431-105 | Antidrive Lever |  |  | 4800 |
| 406-010-432-105 | Antidrive Link |  |  | 4800 |
| 406-076-101-101, -103, -105 | Cyclic Servoactuator | On Condition | 2400 |  |
| TAIL ROTOR CONTROLS |  |  |  |  |
| 406-016-100-109, -115 | Tail Rotor Blade |  |  | 9600 |
| 406-076-102-103 | Actuator | On Condition | 2400 |  |
| HYDRAULIC SYSTEM |  |  |  |  |
| 65016-03, 206-076-030-105 | Pump, Hydraulic | On Condition | On Condition |  |
| DRIVE SYSTEM |  |  |  |  |
| 406-040-007-103, -107, -111 | Main Transmission | 4800 | 2400 |  |
| 406-340-100-101 | Oil Pump | 4800 | 2400 |  |
| 406-040-500-103, -111 | Freewheeling Shaft Assembly | 4800 | 2400 |  |
| 406-040-516-101 | Clutch Input Shaft |  |  | 4800 |
| 406-040-517-101 | Clutch Output Shaft |  |  | 4800 |
| 406-040-400-107, -113 | Tail Rotor Gearbox | 4800 | 2400 |  |
| 406-040-011-105, -107 | Mast Assembly | 4800 | 2400 |  |
| 406-040-040-109 | Main Rotor Mast |  |  | 4800 |
| 406-040-300-105, -107 | Input Driveshaft | 1600 | 1600 | 4800 |
| 406-040-747-101 | Standpipe |  |  | 9600 |
| PYLON SUPPORT COMPONENTS |  |  |  |  |
| 406-010-201-105 | Left Side Beam |  |  | 3030 (NOTE 1, 2) |
| 406-010-202-105 | Right Side Beam |  |  | 3030 (NOTE 1, 2) |
| 406-010-204-101 | Aft Transverse Beam |  |  | 3030 (NOTE 1, 2) |
| 406-010-203-101 | Fwd Transverse Beam |  |  | 3030 (NOTE 1, 2) |
| 406-010-206-107 | Restraint Spring Assembly |  |  | 4800 (NOTE 3) |
| 406-010-217-101 | Corner Mount |  |  | 4800 (NOTE 4) |
| 406-010-232-105, -106 | Restraint Spring Fitting |  |  | 3600 |
| 406-040-052-101 | Transmission Top Case |  |  | 4800 |
| ELECTRICAL SYSTEM |  |  |  |  |
| 406-075-803-101 | AC Generator | 2000 | 2000 |  |
| ARMAMENT |  |  |  |  |
| 7-317141001,622-5646-002, 7-317141001-3, 622-5646-003, 7-317141001-5 622-5646-004 | R H E Unit |  |  | On Condition |
| COCKPIT AIR BAG SYSTEM |  |  |  |  |
| 110160-1 | CPG Side Lateral ITS Assembly |  |  | (NOTE 6) |
| 110160-2 | Pilot Side Lateral ITS Assembly |  |  | (NOTE 6) |
| 110140-1 | Forward Air Bag Module |  |  | (NOTE 6) |
| 107807-1 | Gas Generator |  |  | (NOTE 7) |
| 110190-1 | Gas Generator |  |  | (NOTE 7) |
| NOTES |
| Note 1. Replace at adjusted component hours equal to 3030 or adjusted component landings equal to 5500, whichever occurs first. An adjustment of 3.0 hours and 5.5 landings is required for each autorotation and 0.6 hours and 2.1 for each Hovering autorotation. |
| Note 2. For aircraft flown without the MMS installed, comply with the following: |
| a. Determine the number of actual hours flown without the MMS installed. |
| b. Multiply the flight hours flown without the MMS by 4.8 and substitute this number for the actual hours flown without the MMS towards the retirement life of the side and transverse beams on the MMC Form 719. |
| c. Anytime the aircraft is flown without the MMS installed, comply with steps a and b above. |
| Note 3. Replace at 4800 hours or 9900 landings, whichever occurs first |
| Note 4. Replace at 4800 hours or 20,000 landings, whichever occurs first. |
| Note 5. Deleted |
| Note 6. The air bag modules and lateral ITS assemblies have an operational life of 10 years. This limit can be determined by inspection of the manufacturing date on the nameplate. If date exceeds 10 years, remove and replace the air bag module |
| Note 7. Not to exceed shelf life specified in TB 9-1300-385, Appendix D. The manufacturing date is located on the gas generator flange. The installed life is based on when the packaging hermetic seal is broken. The date the container is opened and the expiration date shall be marked on the main body of the gas generator with an indelible ink marker. |